Directions: The following steps to building a floor are out of order.  First, Put them into order. Write the number of each step on the left. Then discuss each step with a partner by asking questions like, “How do I do that?” or “What tools should you use?”

___A. Snap a chalk line for floor sheathing.

___B. Measure posts, cut and secure them to the piers.

___C. Lay an insulation below sill.

___D. Nail blocks between joists.

___E. Plunge cuts into sill to stretch a dry line for girders.

___F. Nail rim joist flush to sill.

___G. Check the foundation for square and parallel.

___H. Cut sills, drill holes for anchor bolts.

___I. Scatter joists around the building and make safe walkways.

___J. Rolling Joists-turning them up and nailing them in place with two 16 penny nails.

___K. Straighten joists by eye before nailing to intermediate girders.

___L. Insert extra double joists to support interior walls and access spaces.

___M. Attach sills to anchor bolts with a nut and washer, using a wrench.

___N. Cut girders to length on the post.

___O. Nail down girders.

___P. Cut overhanging sheets all at once using a chalk line.

___Q. Lay down sheathing with glue, cutting holes for ducts and plumbing

___R. Pier posts more than 3’ may need braces.

___S. Sight across the foundation wall to be sure sills and girders are flush.

___T. Double-up the side and header joists to make room for stairways and floor ventilation.

Answer: 1-G, 2-H, 3-C, 4-M, 5-E, 6-B, 7-O, 8-N, 9-R, 10-S, 11-F, 12-I, 13-J, 14-D, 15-K, 16-L, 17-T, 18-A, 19-Q, 20-P