Introduction	Page 410

LAN (Local Area Network)

- Computers near one another, usually in the same or neighboring buildings

- Fast connections (10 Mb/sec to 1000 Mb/sec), usually with cables connecting the machines

WAN (Wide Area Network)

- Connects LANS that are far apart, usually over long-distance telephone connections

- Slower connections (56 Kb/sec to 10 Mb/sec), sometimes faster but that gets really expensive

Interoperability

- Networks often have PCs, UNIX, Macintosh, and Novell machines all sharing the same resources

Internet Connection

- Usually a LAN shares a single Internet connection (often a broadband one)

Peer-to-Peer Network

- Called a Workgroup in Microsoft terminology

- Not recommended for more than ten computers

- Each computer runs a desktop operating system such as Win 2000 Pro

- No machine is dedicated to be a server

- Uses Local User Accounts and Local Group Policy

Client-Server Network

- Called a Domain in Microsoft terminology

- Recommended for networks including more than ten computers

- Clients use a desktop operating system such as Win 2000 Pro

- One or more Servers run a server operating system such as Win 2000 Server

- Offers the most advanced networking capabilities such as Active Directory

- More expensive to set up and maintain than a workgroup

  - Usually there are dedicated server computers

  - Server operating systems cost more than desktop operating systems

  - A trained network administrator is needed to set up and maintain the domain

Windows 2000 Networking Versus the OSI Reference Model 	Page 411-412

Skip it – it’s not necessary

NDIS 		Page 412-415

Skip it – it’s not necessary

TCP/IP (Transmission Control Protocol / Internet Protocol)	Pages 415-417

Windows 2000 Pro uses TCP/IP as its default protocol

- This makes LANs work the same way the Internet does

- Your book does into great detail about advanced TCP/IP Features in Win 2000 here, but skip it

NWLink IPX/SPX Compatible Transport	Pages 418-419

- Used to connect with NetWare machines

- The subprotocols used in IPX/SPX include:

  - IPX (Internetwork Packet Exchange): An addressing protocol that assigns numbers to computers, printers, and other network nodes

    - Data is sent in IPX packets

  - SPX (Sequenced Packet Exchange): Provides reliable delivery of IPX packets through sequencing and acknowledgements

  - RIPX (Routing Information Protocol over IPX): announces the existence of routers to the network

- NWLink supports two Application Programming Interfaces (API): tools used to build programs

  - NetBIOS (Network Basic Input Output System):

    - An API that augments the DOS BIOS by adding special functions for local-area networks (LANs)

    - Almost all LANs for PCs are based on the NetBIOS.

  - WinSock (Windows Sockets):

    - An API for Microsoft Windows programs, usually used with TCP/IP

- NWLink alone does not allow a computer running Windows 2000 to access files or printers shared on a NetWare server, or to act as a file or print server to a NetWare client.

  - To access files or printers on a NetWare server, a redirector must be used, such as the Client Service for NetWare on Microsoft® Windows® 2000 Professional, or

  - Gateway Service for NetWare on Microsoft® Windows® 2000 Server.

Netware Interoperability Scenarios (see page 418-419):

- Windows 2000 running NWLink can connect to client/server applications running on a Netware server

- Windows 2000 running NWLink and Client Service for NetWare can connect to Netware file and print servers

- Windows 2000 running NWLink and Gateway Services for NetWare can connect to Netware file and print servers

- NetWare client running IPX with NetBIOS, Named pipes, or Windows Sockets can connect to computers running Windows 2000 (with NWLink) running IPX-aware applications such as SQL Server

- NetWare client running IPX can connect to computers running Windows 2000 Server (with NWLink and File and Print services for NetWare) for file and print services

In-Class Assignment: Ch6a: Networks and Netware with Instant Test	3 pts

- Open Internet Explorer to my Web page: http://fog.ccsf.cc.ca.us/~sbowne/ and click Flash Cards

- Select Ch6a: Networks and Netware and go through them all.  Then take the Instant Test.