The Op-Amp as an Integrator

Consider an op-amp with infinite input resistance and zero output resistance:

Ground the non-inverting input of the op-amp.

Install a capacitor from the output to the inverting input.

- Connect a source vs to the inverting input through a resistor.

The result is an integrator:								 C

C

+   vc  -

R									R

i

-

+			   +

_

+		     +			vi

+			     vo	       vs      _				      		   vo

+						     _

vs							             					                +   AvI          _

_											_

KVL around perimeter gives:	-vs  +   Ri +  1/C (0t i dt  + vc(0) + vo = 0

and noting that			i =  (vs  - vi ) / R  	&	vi = - vo / A

we get					(1 + 1/A) vo =  - 1/RC (0t (vs +  vo /A) dt   -  vc(0)

As   A ((   we get			  vo =  - (1/RC) (0t vs dt  - vc(0)

So now we can see why this element is called an integrator!

The output voltage is proportional to the time integral of the input voltage